# Stationary Concrete Pump MGS 10-60H - MOLI

Description:

MOLI: mobile pipeline concrete pump for long distance concrete delivery.

M.G. Concrete pump Type MGS 10-60H-MOLI, Part no. 9605001

Without a truck / Mounted on a MAN truck model 12.220

### Technical Details:

### Max. output (Rod side)	60 m3/hr

### Max. output (Piston side)	41 m3/hr

### Max. concrete pressure (Rod side)	80 bar

### Max. concrete pressure (Piston side)	120 bar

### Conveying cylinder diameter	180 mm

### Conveying cylinder stroke	1000 mm

Hydraulic pump	Kawasaki K3V140

### Number of strokes (Rod side)	39 stroke/min

### Number of strokes (Piston side)	27 stroke/min

### PTO gear Box 	G61.

Max. Hydraulic pressure for pump group	320 bar

Capacity of oil tank	300 liter

Capacity of water tank	500 liter

Water pump	hydraulic power 20 bar 120 L/min

Hopper	450 liter

Country of origin:	South Korea