# Price Quotation

Date:

To:

Attn:	Mr.

# Item: 	M.G. Concrete Pump MXRZ 52–5.16

Further to your enquiry, please find below our quotation for M52 concrete pump with Roll +Z fold (G + Z) type boom:

Description:

M.G. Concrete pump type MXRZ 52–5.16, Part No. 9525001

Without a truck / Mounted on a XXX truck model XXXX

### Technical Details:

### Max. Concrete capacity:	158 m3/hr

### Max. Concrete pressure:	72 (115) bar

### Hydraulic cylinder diameter:	130/80 mm

### Concrete pumping cylinders:	2100/230 mm

### Main Hydraulic pump	REXROTH HYDROMATIC A11VLO: 260 liter

### Open Hydraulic System

### Transfer gear box:	1:1.19 low ratio

- Oil tank:	550 liters

- Boom control valve proportional	Manufactured by HAWE

- Monoblocks	Manufactured by HAWE

- Water tank:	600 liters

- Hopper capacity:	600 liters

- Water pump	Manufactured by GRUNDFUS: 120liter/min – 20 bar

- Wire remote control:	40 meter

- Oil Cooler	Manufactured by EMMEGI

- Proportional radio remote control	Manufactured by Hetronic

- Central lubrication strip hopper

- Concrete line DN 125 5.5

- Connection for filling water tank

- Chassis horn via remote control & hopper

- Engine speed adjustment from remote control

- Hand held spotlight

- Hinged cast elbow with connection for cleaning

- Operating manuals and spare parts book

- Painting pump: Yellow

- Painting boom: Red

- Aluminum hopper cover

- Rubber collar on hopper

- Set of tools

- Spray hose with bracket

- 4 support plates in magazine

- Tool box

- Towing eye

- Water spray jet with 10 meter hose

Boom specification:

5 arms – “RZ” type

Vertical reach	51.5 meter

Horizontal reach	47.5 meter

Slewing range (Rotation)	365º

Reach depth	37 meters

Unfolding height	9.5 meters

Front support legs width	9.05 meters

Rear support legs width	12.5 meters

Length of end hose	4 meter

X type Outrigger

### Price:

Validity:

Delivery Time:	X weeks from date of order

Payment terms:

Country of origin:	South Korea

Sincerely,