# Price Quotation

Date:

To:

Attn:	Mr.

# Item: 	M.G. Concrete Pump MXZ 28–4.11

Further to your inquiry, please find below our quotation for Z28 concrete pump with Z- fold (Z-type) boom

Description:

M.G. Concrete pump Type MXZ 28–4.11, Part no. 9285001

Without a truck / Mounted on a XXX truck model XXXX

### Technical Details:

### Max. Concrete capacity:	110 m3/hr

### Max. Concrete pressure:	54 (80) bar

### Hydraulic cylinder diameter:	110/63 mm

### Concrete pumping cylinders:	1400/230 mm

### Main Hydraulic pump:	REXROTH HYDROMATIC A11VLO: 145 liter

### Open Hydraulic System

### Transfer gear box:	1:1.12 low ratio

- Oil tank:	400 liters

- Boom control valve proportional:	Manufactured by HAWE

- Monoblocks:	Manufactured by HAWE

- Water tank:	500 liters

- Hopper capacity:	600 liters

- Water pump:	Manufactured by GRUNDFUS: 120liter/min – 20 bar

- Wire remote control:	40 meter

- Oil Cooler:	Manufactured by EMMEGI

- Proportional radio remote control:	Manufactured by Hetronic

- Central lubrication strip hopper

- Concrete line DN 125 5.5

- Connection for filling water tank

- Chassis horn via remote control & hopper

- Engine speed adjustment from remote control

- Hand held spotlight

- Hinged cast elbow with connection for cleaning

- Operating manuals and spare parts book

- Painting pump: Yellow

- Painting boom: Red

- Rubber collar on hopper

- Set of tools

- Spray hose with bracket

- 4 Support plates  in magazine

- Tool box

- Towing eye

- Water spray jet with 10 meter hose

- Aluminum hopper cover

Boom specification:

4 arms – “Z” type

Vertical reach 	27.5 meters

Horizontal reach	23.5 meters

Slewing range (Rotation)	370º

Reach depth	 17 meters

Unfolding height	6.5 meters

Front support legs width	6.2 meters

Rear support legs width	25 meters

Length of end hose	4 meters

“X” type Outrigger

### Price:

Validity:

Delivery Time:	X weeks from date of order

Payment terms:

Country of origin:	South Korea

Sincerely,

M. Gold Assets & Holdings Ltd