# Price Quotation

Date:

To:

Attn:	Mr.

# Item:	M.G. Concrete Pump MXZR21–4.12

Further to your enquiry, please find below our quotation for M21 concrete pump with Z + roll fold (Z + G) type boom:

Description:

M.G. Concrete pump Type MXZR21–4.12, Part No. 9215001

Without a truck / Mounted on a XXX truck model XXXX

### Technical Details:

### Max. Concrete capacity:	120 m3/hr

### Max. Concrete pressure:	54 (80) bar

### Hydraulic cylinder diameter:	110/63 mm

### Concrete pumping cylinders:	1400/200 mm

### Main Hydraulic pump	KAWASAKI 180 liter

### Open Hydraulic System

### Transfer gear box:	1:1.12 low ratio

- Oil tank:	480 liter

- Boom control valve proportional	Manufactured by HAWE

- Monoblocks	Manufactured by HAWE

- Water tank:	600 liter

- Hopper capacity:	450 liter

- Water pump:	Manufactured by GRUNDFUS: 120liter/min – 20 bar

- Wire remote control:	40 meter

- Oil Cooler:	Manufactured by EMMEGI

- Proportional radio remote control:	Manufactured by Hetronic

- Central lubrication strip hopper

- Concrete line DN 125 5.5

- Connection for filling water tank

- Chassis horn via remote control & hopper

- Engine speed adjustment from remote control

- Hand held spotlight

- Hinged cast elbow with connection for cleaning

- Operating manuals and spare parts book

- Painting pump: Yellow

- Painting boom: Red

- Aluminum hopper cover

- Rubber collar on hopper

- Set of tools

- Spray hose with bracket

- Support plates 4 x in magazine

- Tool box

- Towering eye

- Water spray jet with 10 meter hose

Boom specification:

4 arms – “Z+G” type

Vertical reach	20.46 meter

Horizontal reach	17.2 meter

Slewing range (Rotation)	365º

Reach depth	8.1 meter

Unfolding height	4.5 meter

Front support legs width   	3.8 meter

Rear support legs width	2.5 meter

Length of end hose	3 meter

“X” type Outrigger

### Price:

Validity:

Delivery Time:

Payment terms:

Country of origin:	South Korea

Sincerely,

M. Gold Assets & Holdings Ltd