# Price Quotation

Date:

To:

Attn:	Mr.

# Item:	M.G. Concrete Pump MXZR43–5.16

Further to your enquiry, please find below our quotation for M43 concrete pump with Z + roll fold (Z + G) type boom:

Description:

M.G. Concrete pump Type MXZR43–5.16, Part No. 9435001

Without a truck / Mounted on a XXX truck model XXXX

### Technical Details:

### Max. Concrete capacity:	158 m3/hr

### Max. Concrete pressure:	72 (115) bar

### Hydraulic cylinder diameter:	130/80 mm

### Concrete pumping cylinders:	2100/230 mm

### Main Hydraulic pump	REXROTH HYDROMATIC: A11VO 260 liter

### Open Hydraulic System

### Transfer gear box:	1:1.19 low ratio

- Oil tank:	550 liter

- Boom control valve proportional	Manufactured by HAWE

- Monoblocks	Manufactured by HAWE

- Water tank:	500 liter

- Hopper capacity:	600 liter

- Water pump:	Manufactured by GRUNDFUS: 120liter/min – 20 bar

- Wire remote control:	40 meter

- Oil Cooler:	Manufactured by EMMEGI

- Proportional radio remote control:	Manufactured by Hetronic

- Central lubrication strip hopper

- Concrete line DN 125 5.5

- Connection for filling water tank

- Chassis horn via remote control & hopper

- Engine speed adjustment from remote control

- Hand held spotlight

- Hinged cast elbow with connection for cleaning

- Operating manuals and spare parts book

- Painting pump: Yellow

- Painting boom: Red

- Aluminum hopper cover

- Rubber collar on hopper

- Set of tools

- Spray hose with bracket

- Support plates 4 x in magazine

- Tool box

- Towering eye

- Water spray jet with 10 meter hose

Boom specification:

5 arms – “Z+G” type

Vertical reach	42.3 meter

Horizontal reach	39.3 meter

Slewing range (Rotation)	365º

Reach depth	26 meter

Unfolding height	7.8 meter

Front support legs width   	7.8 meter

Rear support legs width	8.6 meter

Length of end hose	4 meter

“X” type Outrigger

### Price:

Validity:

Delivery Time:

Payment terms:

Country of origin:	South Korea

Sincerely,

Drawing with truck: