# Price Quotation

Date:

To:

Attn:	Mr.

# Item: 	M.G. Concrete Pump MXR 36–4.16

Further to your inquiry, please find below our quotation for M36 concrete pump with R-fold (R-type) boom

Description:

M.G. Concrete pump Type MXR 36–4.16, Part no. 9365001

Without a truck / Mounted on a XXX truck model XXXX

### Technical Details:

### Max. Concrete capacity:	158 m3/hr

### Max. Concrete pressure:	72 (115) bar

### Hydraulic cylinder diameter:	130/80 mm

### Concrete pumping cylinders:	2100/230 mm

### Main Hydraulic Pump	REXROTH HYDROMATIC A11VLO 260 liter

### Open Hydraulic System

### Transfer gear box:	1:1.19 low ratio

- Oil tank:	550 liters

- Boom control valve proportional	Manufactured by HAWE

- Monoblocks	Manufactured by HAWE

- Water tank:	600 liters

- Hopper capacity:	600 liters

- Water pump	Manufactured by GRUNDFUS: 120liter/min – 20 bar

- Wire remote control:	40 meter

- Oil Cooler	Manufactured by EMMEGI

- Proportional radio remote control	Manufactured by Hetronic

- Central lubrication strip hopper

- Concrete line DN 125 5.5

- Connection for filling water tank

- Chassis horn via remote control & hopper

- Engine speed adjustment from remote control

- Hand held spotlight

- Hinged cast elbow with connection for cleaning

- Operating manuals and spare parts book

- Painting pump: Yellow

- Painting boom: Red

- Rubber collar on hopper

- Set of tools

- Spray hose with bracket

- 4 Support plates  in magazine

- Tool box

- Towing eye

- Water spray jet with 10 meter hose

- Aluminum hopper cover

Boom specification:

4 arms – “R” type

Vertical reach 	35.8 meters

Horizontal reach	32.1 meters

Slewing range (Rotation)	370º

Reach depth	24 meters

Unfolding height	8.6 meters

Front support legs width	6.3 meters

Rear support legs width	8.5 meters

Length of end hose	4 meters

“X” type Outrigger

### Price:

Validity:

Delivery Time:	X weeks from date of order

Payment terms:

Country of origin:	South Korea

Sincerely,

M. Gold Assets & Holdings Ltd